## Slide 1
RENEWABLE TELEMETRY · AI DIAGNOSTICS · CHAOS ENGINEERING
GridSentry AI
An End-to-End Platform for Wind, Solar & Weather Intelligence
DEPI
رواد مصر الرقمية
Supervised By ENG : Sara Ashraf
Notes: 1

## Slide 2
DEPI
رواد مصر الرقمية
PRESENTED BY
Mohamed Hany
Michael Samy
Hana Alaa
Nada Hossam
Toqa Hussein
Notes: 1

## Slide 3
PRESENTATION ROADMAP
What We'll Cover — Five Speakers
01
System Overview & Architecture
What DEPI Grid is and how its pieces fit together
02
Data Pipeline
Kafka streaming, direct-DB simulation, TimescaleDB persistence
03
AI / ML Inference Engine
Forecasting models, anomaly detection, soiling diagnostics
04
API, Dashboard & RAG
FastAPI orchestration, Streamlit UI, Gemini-powered repair blueprints
05
Engineering, Setup & Lessons
Design decisions, run instructions, troubleshooting playbook
02
Notes: 2

## Slide 4
01
PART ONE
System Overview & Architecture
The big picture: what DEPI Grid does and how five subsystems connect.
Notes: 3

## Slide 5
PART 01 · OVERVIEW
What Is DEPI Grid?
An end-to-end renewable-energy monitoring platform combining real-time telemetry streaming, machine-learning forecasting, explainable anomaly detection, and Retrieval-Augmented Generation (RAG) for autonomous repair blueprints.
•
Three live data sources
Wind, Solar & Weather telemetry unified in one pipeline
•
Streaming + storage
Kafka ingestion into TimescaleDB time-series tables
•
Hybrid AI engine
ONNX / scikit-learn forecasting and anomaly detection
•
Generative diagnostics
Gemini + FAISS RAG produces step-by-step repair blueprints
PLATFORM AT A GLANCE
1
Simulation / Kafka
Ingests synthetic sensor data
2
TimescaleDB
Stores time-series telemetry
3
FastAPI Orchestrator
REST endpoints for forecasts & diagnostics
4
ONNX + scikit-learn
Power forecasting & anomaly detection
5
Gemini + FAISS
RAG-generated repair blueprints
6
Streamlit Dashboard
Live grid balance & explainable diagnostics
04
Notes: 4

## Slide 6
PART 01 · OVERVIEW
Architecture at a Glance
CSV / Simulation
Kafka Producer
Kafka Topics
wind · solar · weather
Kafka Consumer
TimescaleDB
batched inserts
FastAPI Orchestrator
ONNX Forecasting
wind / solar / demand
Anomaly Detection
Isolation Forest
Gemini + FAISS
RAG blueprints
Streamlit Dashboard
grid balance · AI forecasts · explainable diagnostics
WHY THIS SHAPE
Ingestion and persistence run independently of the API layer, so the FastAPI orchestrator only ever reads from TimescaleDB. This decouples streaming cadence from request latency, and lets forecasting, anomaly detection, and RAG diagnostics execute as parallel branches off a single source of truth.
05
Notes: 5

## Slide 7
02
PART TWO
The Data Pipeline
How synthetic telemetry is generated, streamed, and persisted at scale.
Notes: 6

## Slide 8
PART 02 · DATA PIPELINE
Ingestion: Two Ways In
sender.py
Tri-Stream Kafka Producer
Reads three simulation CSVs (Wind, Solar, Weather) in parallel threads and streams each row to its Kafka topic with a live UTC timestamp.
start_multi_sender() launches 3 daemon threads — one per telemetry stream — and joins them
stream_data() injects a live ts field and produces JSON keyed for partitioning
SIMULATION_SPEED controls emission cadence between rows
delivery_report() logs Kafka delivery failures
simulation.py
Direct-to-DB Fallback Generator
A standalone simulator that bypasses Kafka entirely and writes synthetic telemetry directly into TimescaleDB every 10 seconds — ideal for quick local testing.
get_solar_irradiance(hour): bell-curve profile peaking at solar noon — zero outside 06:00–18:00
Formula: 1000 × sin((hour−6)×π/12) with ±50 W/m² noise
simulate_and_insert() writes one synchronized Wind + Solar + Weather snapshot per transaction
Runs indefinitely, once every 10 seconds
07
Notes: 7

## Slide 9
PART 02 · DATA PIPELINE
Persistence & Resource Constraints
receiver.py
Kafka Consumer → TimescaleDB Writer
Subscribes to all three telemetry topics with a manual-commit consumer (auto.offset.reset='earliest'). Records are buffered per topic; once a buffer reaches BATCH_SIZE, they're bulk-inserted with execute_values, the DB transaction commits, then the Kafka offset commits synchronously — giving at-least-once delivery semantics.
4GB
WSL2 RAM cap — architecture tuned to stay within it
Batches of 5
receiver.py commit size — prevents memory spikes
30 days
TimescaleDB retention — raw hypertables auto-discard older telemetry
CONTINUOUS AGGREGATES
Materialized views reduce query load for ML models by pre-compiling rollups:
Solar metrics
15-minute rollups
Wind metrics
1-hour rollups
08
Notes: 8

## Slide 10
03
PART THREE
The AI / ML Inference Engine
Forecasting, anomaly detection, and the models that keep the grid explainable.
Notes: 9

## Slide 11
PART 03 · AI / ML ENGINE
inference.py — Forecasting & Anomaly Core
Central module loading ONNX / scikit-learn models, with graceful rule-based and physics-based fallbacks whenever a model output looks implausible.
Wind · Anomaly
detect_wind_anomaly()
Rule pre-check on extreme deviation/vibration, then a scaled 4-feature Isolation Forest.
Wind · Forecast
predict_wind_power()
ONNX LSTM forecast (kW); falls back to power = wind_speed³ × 0.85 if output is near-zero.
Solar · Forecast
predict_solar_yield()
ONNX Transformer forecast with daylight gate; falls back to irradiance × 2.1 × noise.
Solar · Anomaly
detect_solar_anomaly()
Maps schema to training features and flags anomalies when the Isolation Forest predicts −1.
Demand · Forecast
predict_grid_demand()
Weather-driven ONNX model; falls back to time-of-day heuristic bands below 100 kW.
Infrastructure
ModelRegistry
Lazy-loading singleton cache keyed by path — avoids re-loading pkl/ONNX per request.
10
Notes: 10

## Slide 12
PART 03 · AI / ML ENGINE
Deep Dive: Model Architecture
SOLAR · MULTI-TASK TRANSFORMER
MultiTaskSolarForecaster
Encoder
d_model=64 · nhead=4 · 3 layers · FFN 256
Input window
96 timesteps (24h @ 15-min) × 7 features
Output horizon
16 future timesteps (4 hours)
Regression head
HuberLoss (δ=1.0) → AC_POWER, robust to spikes
Classification head
BCELoss + Sigmoid → Active/Producing state
Optimization
AdamW + ReduceLROnPlateau + Early Stopping
Export
Traced to ONNX (opset 14), dynamic batch axis
PREPROCESSING
Cyclical hour encoding: sin/cos of 2π×hour/24
Daylight masking at IRRADIATION > 0.05 W/m²
StandardScaler fit & saved for identical live transform
Chronological 70/15/15 train/val/test split
SOLAR SOILING & DEGRADATION ENGINE
HistGradientBoostingRegressor predicts "perfect" DC_POWER from irradiation and temperatures; the gap to actual output becomes a diagnostic signal.
15%
efficiency-loss threshold
72 hrs
rolling window (288 × 15-min)
11
Notes: 11

## Slide 13
04
PART FOUR
API, Dashboard & RAG
Turning model outputs into live visuals and Gemini-authored repair instructions.
Notes: 12

## Slide 14
PART 04 · API & DASHBOARD
main.py — FastAPI Orchestrator
The API gateway wiring together the database, ML inference, FAISS vector store, and the Gemini LLM.
GET
/
Health check
GET
/grid/live
Latest 30 rows of wind & solar telemetry, descending
GET
/grid/forecast
Last 24 rows across all tables → runs all 3 ML models → surplus/deficit status
POST
/diagnose/{asset_type}/{asset_id}
Anomaly check; if flagged, retrieves top-4 FAISS excerpts and prompts Gemini for a repair blueprint
POST
/grid/inject_anomaly/{asset_type}
Chaos engineering: inserts a future-timestamped extreme telemetry row
13
Notes: 13

## Slide 15
PART 04 · API & DASHBOARD
The RAG Diagnostic Engine
When an anomaly fires, DEPI Grid moves from detection to explanation — retrieving real manual excerpts and asking Gemini to write the fix.
1
Ingest OEM Manuals
PyPDFLoader reads hardware manuals (e.g. ABB PVS800); RecursiveCharacterTextSplitter chunks text into 1,500-char pieces with 200-char overlap.
2
Embed & Store
Chunks embedded via models/gemini-embedding-001, persisted to FAISS or Chroma. Batches throttled ~65s per 90 chunks for rate limits.
3
Retrieve on Anomaly
RAGDiagnosticEngine fetches the top-K most relevant excerpts for the flagged asset and fault type.
4
Generate Blueprint
gemini-flash-latest (temp = 0.0) returns strict JSON: STATUS, ERROR_CODE, METRIC_EXPLANATION, RECOMMENDED_ACTION.
Final response is stripped of Markdown fences and parsed into a strict dictionary so the Streamlit dashboard can render it safely.
14
Notes: 14

## Slide 16
PART 04 · API & DASHBOARD
dashboard.py — The Streamlit Control Panel
Sidebar Control Panel
Toggles live data sync and offers a Fault Injection dropdown that triggers /grid/inject_anomaly and auto-launches a diagnostic scan.
Grid Balance Meter
Computes generation-vs-demand ratios and renders a custom HTML/CSS bar showing Surplus (green) or Deficit (red).
Live Telemetry Graphs
Dual-trace Plotly charts: solid line for physics-derived actual power, dashed line for AI forecast history from session state.
Diagnostic Center
Two-column UI for manual or auto-scan results — anomaly badges plus a text area rendering the RAG repair blueprint.
15
Notes: 15

## Slide 17
05
PART FIVE
Engineering, Setup & Lessons Learned
Why the system is built this way, how to run it, and what broke along the way.
Notes: 16

## Slide 18
PART 05 · ENGINEERING & SETUP
Key Engineering Decisions
CONCERN
DECISION
RATIONALE
Model loading
ModelRegistry cache
Avoids re-loading pkl/ONNX every request; safe under threaded handling
Consumer commits
Manual, synchronous
At-least-once delivery — no data loss if the consumer crashes pre-commit
Forecast fallbacks
Physics-based heuristics
Keeps the dashboard continuous if ONNX inference returns implausible values
RAG context
FAISS local + Gemini
Deterministic retrieval combined with creative synthesis, offline fallback included
Async diagnostics
run_in_threadpool
Keeps the event loop unblocked while sklearn/ONNX inference runs synchronously
Solar daylight gate
Hour-based zero output
Prevents spurious nighttime solar predictions from the Transformer model
Chaos injection
Future-timestamped row
Guarantees the anomaly is the most-recent record, avoiding race conditions
17
Notes: 17

## Slide 19
PART 05 · ENGINEERING & SETUP
How to Run the Platform
PREREQUISITES: Python 3.10+ · Docker Desktop (Kafka, Zookeeper, TimescaleDB) · Git
1
Start Infrastructure
Bring up Docker containers for Kafka, Zookeeper, and TimescaleDB/PostgreSQL.
2
Stream Telemetry
Method A: sender.py + receiver.py (Kafka path) · Method B: simulation.py (direct-DB, quick test).
3
Launch the API
python src/api/main.py — starts uvicorn on 127.0.0.1:8000.
4
Launch the Dashboard
streamlit run src/ui/dashboard.py
18
Notes: 18

## Slide 20
PART 05 · ENGINEERING & SETUP
Troubleshooting & Known Issues
SYMPTOM
Graphs zig-zagging in time
Root cause: sender.py looped historical CSVs infinitely, jumping timestamps backward
Fix: Removed the infinite loop; queries now align to NOW() for live sync
SYMPTOM
ONNX shape-mismatch crash
Root cause: Models require exact tensor shapes (e.g. expecting 144×10, given only 24×1)
Fix: Dynamically read required dims and build padded zero-matrices to match
SYMPTOM
Dashboard won't open browser
Root cause: config.toml had headless = true, meant for cloud deployments
Fix: Set headless = false for local development
SYMPTOM
Injected anomaly not detected
Root cause: Race condition — fresh normal rows push the anomaly down before it's read
Fix: Apply a +30s UTC offset so injected rows sort first, every time
19
Notes: 19

## Slide 21
IN SUMMARY
A Reference Architecture for Intelligent, Scalable Renewable Energy
High-frequency Kafka streaming with batched TimescaleDB persistence keeps data flowing without overwhelming local hardware. A hybrid ML engine balances deterministic physics-based heuristics with ONNX neural networks for reliable forecasting. And by embedding Chaos Engineering alongside RAG-augmented generative AI, DEPI Grid moves beyond monitoring — delivering explainable diagnostics and autonomous repair blueprints in real time.
Kafka Streaming
TimescaleDB
ONNX + scikit-learn
Gemini + FAISS RAG
Streamlit
Chaos Engineering
DEPI Grid — Team Presentation
Notes: 20

## Slide 22
DEPI Grid — Team Presentation
Thank you..!
Any Questions..?
رواد مصر الرقمية
DEPI
Notes: 20